## Slide 1: Supply Voltage Biasing
Andy Whetzel and Elena Weinberg
University of Virginia

## Slide 2: Agenda
Background
  FinFET technology
Problem and approach
Our design
Implementation
Results
Discussion
Conclusion

## Slide 3: Background
FinFET Technology
Scalable
Higher drive strength per unit silicon
Image from: http://www.ece.uc.edu/~kroenker/Research/Research%20Project%20Summaries/FINFET_image004.jpg
Image from: http://www.siliconsemiconductor.net/images/news/image-76523-2012-12-12.jpg

## Slide 4: Problem
Body biasing does not work on FinFETs
MOSFET vs. FinFET:
https://www.semiwiki.com/forum/content/attachments/5665d1355855218-planar-vs.-3d-finfet.jpg
Notes: FinFETs resistant to body effects

## Slide 5: Approach
Supply voltage biasing with FreePDK
Contributions:
Our design for supply voltage biasing
A new knob
A new technique for decreasing delay in integrated circuits (ICs) implementing FinFET technology

## Slide 6: Supply Biased Inverter Gate

## Slide 7: Ring Oscillator
11 Inverters
Swept bias voltage from -0.1 V to 0.1 V
  1.1 V nominal
Measured frequency, active power, and static power vs. bias voltage

## Slide 8: Ring Oscillator Results
Chart: Frequency vs. Supply Bias
| -0.1 | -0.09 | -0.08 | -0.07 | -0.06 | -0.05 | -0.0399999999999999 | -0.0299999999999999 | -0.0199999999999999 | -0.00999999999999991 | 0.0 | 0.01 | 0.02 | 0.03 | 0.04 | 0.05 | 0.06 | 0.07 | 0.08 | 0.09 | 0.1
 | 0.72612 | 0.75745 | 0.78831 | 0.81847 | 0.8478 | 0.87607 | 0.90329 | 0.92944 | 0.95429 | 0.97785 | 1 | 1.0209 | 1.0401 | 1.0577 | 1.0737 | 1.088 | 1.1005 | 1.1112 | 1.12 | 1.1271
Chart: Active Power vs. Supply Bias
| -0.1 | -0.09 | -0.08 | -0.07 | -0.06 | -0.05 | -0.0399999999999999 | -0.0299999999999999 | -0.0199999999999999 | -0.00999999999999991 | 0.0 | 0.01 | 0.02 | 0.03 | 0.04 | 0.05 | 0.06 | 0.07 | 0.08 | 0.09 | 0.1
 | 0.63392 | 0.66553 | 0.69799 | 0.73174 | 0.76677 | 0.80222 | 0.83981 | 0.87783 | 0.91713 | 0.95814 | 1 | 1.044 | 1.0893 | 1.1375 | 1.1875 | 1.2409 | 1.2986 | 1.3622 | 1.4331 | 1.5139 | 1.6087
Chart: Static Power vs. Supply Bias
| -0.1 | -0.09 | -0.08 | -0.07 | -0.06 | -0.05 | -0.0399999999999999 | -0.0299999999999999 | -0.0199999999999999 | -0.00999999999999991 | 0.0 | 0.01 | 0.02 | 0.03 | 0.04 | 0.05 | 0.06 | 0.07 | 0.08 | 0.09 | 0.1
 | 1.2036 | 1.041 | 0.9163 | 0.82183 | 0.75281 | 0.70718 | 0.68493 | 0.69021 | 0.73148 | 0.82527 | 1 | 1.302 | 1.8058 | 2.6278 | 3.9509 | 6.0491 | 9.3304 | 14.4004 | 22.1119 | 33.662 | 50.5847

## Slide 9: NAND and NOR Gates
Designed similarly to supply biased inverter
  Double the transistors, one high and one low output
Setup in ring oscillator configuration such that high output is tied to NMOS and low output is tied to PMOS in subsequent gate
Results were similar, therefore we obtained the motivation to pursue combinational logic other than a ring oscillator

## Slide 10: Full Adder

## Slide 11: 8 Bit Ripple Carry Adder
Chart: Delay vs. Supply bias
| -100.0 | -90.0 | -80.0 | -70.0 | -60.0 | -50.0 | -40.0 | -30.0 | -20.0 | -10.0 | 0.0 | 10.0 | 20.0 | 30.0 | 40.0 | 50.0 | 60.0 | 70.0 | 80.0 | 90.0 | 100.0
Delay (ps) | 1.4224 | 1.3534 | 1.2931 | 1.2414 | 1.1897 | 1.1466 | 1.1121 | 1.0776 | 1.0517 | 1.0259 | 1 | 0.97414 | 0.9569 | 0.93966 | 0.92241 | 0.90517 | 0.89655 | 0.88793 | 0.87069 | 0.87069 | 0.86207
Chart: Static Power vs. Supply Bias
| -100.0 | -90.0 | -80.0 | -70.0 | -60.0 | -50.0 | -40.0 | -30.0 | -20.0 | -10.0 | 0.0 | 10.0 | 20.0 | 30.0 | 40.0 | 50.0 | 60.0 | 70.0 | 80.0 | 90.0 | 100.0
 | 0.85453 | 0.77493 | 0.71383 | 0.66846 | 0.63761 | 0.62129 | 0.62189 | 0.64517 | 0.70149 | 0.80935 | 1 | 1.3248 | 1.8663 | 2.7562 | 4.197 | 6.5015 | 10.1473 | 15.8408 | 24.6368 | 38.0299 | 58.1891
Chart: Switching Power vs. Supply Bias
| -100.0 | -90.0 | -80.0 | -70.0 | -60.0 | -50.0 | -40.0 | -30.0 | -20.0 | -10.0 | 0.0 | 10.0 | 20.0 | 30.0 | 40.0 | 50.0 | 60.0 | 70.0 | 80.0 | 90.0 | 100.0
 | 0.65976 | 0.67386 | 0.69165 | 0.7137 | 0.74031 | 0.77165 | 0.80787 | 0.84882 | 0.8937 | 0.94409 | 1 | 1.0622 | 1.1323 | 1.2087 | 1.2937 | 1.3898 | 1.4992 | 1.6244 | 1.7724 | 1.9496 | 2.1677
Chart: Static Power vs. Reverse Supply Bias
| -100.0 | -90.0 | -80.0 | -70.0 | -60.0 | -50.0 | -40.0 | -30.0 | -20.0 | -10.0 | 0.0
 | 0.85453 | 0.77493 | 0.71383 | 0.66846 | 0.63761 | 0.62129 | 0.62189 | 0.64517 | 0.70149 | 0.80935 | 1

## Slide 12: Discussion
Our design shows potential to reduce delay in ICs
Trade-offs:
Area
Power

## Slide 13: Conclusion
We successfully designed and implemented a new knob
Our design decreases delay in ICs implementing FinFET technology
Area and power trade-offs
Future Work
Further investigation of static and switching power in FinFETs under supply bias
Explore accuracy of gate induced drain leakage (GIDL)
Generating bias voltages

## Slide 14: Questions?

## Slide 15
Image from: http://www.synopsys.com/Company/Publications/SynopsysInsight/Pages/Art2-finfet-challenges-ip-IssQ3-12.aspx